## Slide 1: TITLE : Solar-Powered Smart Mobile Charger
SPARKATHON
TEAM NAME : SUN CHASERS
Subtitle:
A Sustainable Charging Solution for Remote and Outdoor Areas .
TEAM MEMBERS:
NARMATHA . A
AMIRTHA . U
SANTHIYA . T
SIVA DHARSHINI
SWETHA . K
SUBHASHINI . S

## Slide 2: Problem & Solution
Problem:
In remote areas and during outdoor activities, there is limited access to reliable charging solutions for mobile devices.
Solar-powered chargers offer an eco-friendly and sustainable alternative.
Solution:
A solar-powered mobile charger that uses solar energy to charge devices, with real-time monitoring of the system’s performance

## Slide 3: SYSTEM COMPONENTS
Solar Panel (6V-12V): Converts sunlight to DC power for charging.
Li-ion Battery (3.7V): Stores energy generated by the solar panel.
TP4056 Battery Protection Circuit: Protects the battery from overcharging and overdischarging.
LM2596 Buck Converter: Steps down the voltage to 5V for charging devices.
ACS712 Current Sensor: Monitors the current drawn from the battery.
ESP32 Microcontroller: Manages system operations and controls the display.
OLED Display (0.96-inch): Displays real-time information like battery status and charging progress.

## Slide 4: WORKING PRINCIPLE
How it Works:
  The solar panel generates energy from sunlight and charges the Li-ion battery.
  The LM2596 buck converter provides a stable 5V output for charging mobile devices.
  The ESP32 controls and monitors the system, displaying data on the OLED screen like battery voltage, solar panel voltage, and current draw.
  ACS712 measures the current for real-time monitoring.

## Slide 5: Key Features & Benefits
Portable & Sustainable:
  Ideal for outdoor activities like camping, hiking, and remote areas.
  Powered by solar energy, reducing reliance on traditional power sources.
Efficient & Safe:
  Features battery protection, current monitoring, and voltage regulation for safe and efficient charging.
Real-Time Monitoring:
  OLED display shows key data for users to monitor battery levels, current flow, and solar panel performance.

## Slide 6
CONCLUSION
The Solar-Powered Smart Mobile Charger is an innovative, eco-friendly solution to power mobile devices in remote areas.
It combines solar energy, real-time monitoring, and safe charging into a portable and practical product.
Next Steps:
Future improvements could include adding an MPPT charge controller for better efficiency, wireless charging features, and higher-capacity batteries for longer usage.
THANK YOU